## Slide 1: Synthesis of SFQ Circuits with Compound Gates
Rassul Bairamkulov, Alessandro Tempia Calvino, and Giovanni De Micheli
Integrated Systems Laboratory, EPFL
October 17, 2023
Download manuscript PDF
Notes: Add names of authors

## Slide 2: OUTLINE
Motivation
Rapid Single-Flux Quantum – Overview
Gate Compounding Technique
Summary
Notes: Remove

## Slide 3: High-Performance Computing
Performance grows exponentially
  +25% yearly
Most due to parallelization
Single-thread performance grows at a slower pace
  +5-15% yearly
Many algorithms are poorly parallelized
  Iterative optimization
  Cryptography
  Data compression
M. Lechner, “Evolution of Single-threaded x86 CPU Performance”, 2020
https://www.top500.org/statistics/perfdevel/
Notes: Remove

## Slide 4: Rapid Single-Flux Quantum
Rapid Single-Flux Quantum
  Invented in 1985 by K. Likharev and V. Semenov [1]
Superconductive technology
  Based on Josephson Junctions
  Cryogenic, 4.2 K
Low-power
  Hence low heat
  Even considering refrigeration
World’s fastest digital technology
  Record speed of 770 GHz [2]
  Consistently achieving speeds above 10 GHz
[1] K. K. Likharev and V. K. Semenov, RSFQ logic/memory family: a new Josephson-junction technology for sub-terahertz-clock-frequency digital systems, in IEEE TASC 1991
[2] W. Chen, et al. Rapid single flux quantum T-flip flop operating up to 770 GHz. IEEE TASC 1999.
[3] D. S. Holmes, et al. Energy-efficient superconducting computing—Power budgets and requirements. IEEE TASC 2013.
Switching
power, µW
Switching delay, ps
Notes: mention pulse-based logic
mention that the plot is for single gate
Explain that presence/absence is 0/1
registers easy to do
inversion is hard
Explain gate compounding first
Traditionally - on safe side

## Slide 5: RSFQ: Challenges
Fabrication technology
  State of the art : 6k JJ/mm2
  Compare to 90M transistors/mm2 (TSMC 7nm)
Expensive memory
  Poor density of inductor-based memory
Architectural differences
  Gate-level pipelining

## Slide 6: Path Balancing
A
B
C
D
E
Ensure correct order of signal arrival
Fundamental issue in superconductive electronics

## Slide 7: Path Balancing
A
B
C
D
E
Ensure correct order of signal arrival
Fundamental issue in superconductive electronics
  Dominates the IC area
Notes: In general
clocking at every gate
needs sync input
I consider gate

## Slide 8: OUTLINE
Motivation
Rapid Single-Flux Quantum – Overview
Gate Compounding Technique
Summary

## Slide 9: Josephson Junction (JJ)
I0
😴
I0
I0
Ic
V
Ic
L
Superconductor
Insulator
Superconductor
Notes: Illinois edu physics498 sqd

## Slide 10: Josephson Junction (JJ)
I0
I0
Ic
V
Ic
L
I0
😕
Notes: Illinois edu physics498 sqd

## Slide 11: Josephson Junction (JJ)
I0
I0
Ic
V
Ic
L
I0
😲
~2mV
~1ps
Notes: Static

## Slide 12: Basic JJ SQUID Loop
I0
J0
J1
A
B
Logic 0
Notes: Mention that it's called SQUID

## Slide 13: Basic JJ Loop
I0
J0
J1
A
B
Logic 0
Notes: Mention that it's called SQUID

## Slide 14: Basic JJ Loop
I0
J0
J1
A
B
Logic 1
Notes: Mention that it's called SQUID

## Slide 15: D flip-flop
CLK
I0
J0
J1
D
Q
J2
Logic 1
Notes: Mention that it's called SQUID

## Slide 16: D flip-flop
CLK
I0
J0
J1
J2
Logic 1
D
Q
Notes: Mention that it's called SQUID

## Slide 17: D flip-flop
CLK
I0
J0
J1
J2
Logic 0
D
Q
Notes: Mention that it's called SQUID

## Slide 18: D flip-flop
CLK
I0
J0
J1
J2
Logic 0
D
Q
Notes: Mention that it's called SQUID

## Slide 19: Inverter
I0
A
CLK
Q
Notes: Mention that it's called SQUID

## Slide 20: Inverter
I0
A
Q
CLK
Notes: Mention that it's called SQUID

## Slide 21: Inverter
I0
A
Q
CLK
Notes: Mention that it's called SQUID

## Slide 22: Merger (Asynchronous OR)
I0
Q
B
A
Notes: Mention that it's called SQUID

## Slide 23: Merger (Asynchronous OR)
I0
Q
B
A
Notes: Mention that it's called SQUID

## Slide 24: AND Gate
I0
Q
B
A
Notes: Mention that it's called SQUID

## Slide 25: AND Gate
I0
Q
B
A
Notes: A

## Slide 26: AND Gate
I0
Q
B
A
Notes: B

## Slide 27: AND Gate
I0
Q
B
A
CLK
CLK
Notes: B

## Slide 28: OUTLINE
Motivation
Rapid Single-Flux Quantum – Overview
Gate Compounding Technique
Summary

## Slide 29: RSFQ Elements
Behavior in RSFQ
Function
RSFQ Symbol
NOT
XOR
AND
OR*
CB
OR
Notes: Mention that it's called SQUID

## Slide 30: Three Types of SFQ Devices
Asynchronous
  Asynchronous input
  Asynchronous output
CB
s
Synchronizers
  Asynchronous input
  Synchronized output
Synchronized
  Synchronized input
  Asynchronous output
Notes: classifying the gates into three categories

## Slide 31: Three Types of SFQ Devices
Asynchronous
  Asynchronous input
  Asynchronous output
CB
s
Synchronizers
  Asynchronous input
  Synchronized output
Synchronized
  Synchronized input
  Asynchronous output
AA
AS
SA

## Slide 32: Gate Compounding Technique
AA
AS
SA
AA
CB
s
CB
s
AS right before SA
  Synchronize inputs to SA gates
AA gates at periphery
  Enrich functionality without extra cycles
R. Bairamkulov and G. De Micheli, "Compound Logic Gates for Pipeline Depth Minimization in Single Flux Quantum Integrated Systems," Proc. GLSVLSI 2023
Notes: DFF - introduce DFF
AND/OR - highlight the need for sync inputs

## Slide 33: Gate Compounding: Example
SA gates sensitive to input timing
  Place them after AS gates
A
B
CLK
Q
CLK
I0
AS
AS
SA
Conventional RSFQ AND gate
Q=AB
Notes: Move before

## Slide 34: Gate Compounding: NIMPLY
Replace DFF with inverter
A
B
CLK
Q
CLK
I0
Q=AB

## Slide 35: Gate Compounding: XNOR
s
s
CB
CB
AS
AA
SA
AA

## Slide 36: Case Study: 4-bit Brent Kung Adder
Gate compounding [4]
  4 clock cycles
  658 JJs
Conventional gates [5]
  6 clock cycles
  928 JJs
[4] R. Bairamkulov and G. De Micheli. "Compound Logic Gates for Pipeline Depth Minimization in Single Flux Quantum Integrated Systems." Proc. GLSVLSI 2023.
[5] T. Kawaguchi, K. Takagi, and N. Takagi. 2021. Rapid Single-Flux-Quantum Logic Circuits Using Clockless Gates. IEEE TASC Vol. 31, No. 4 2021.

## Slide 37: Technology Mapping 101
Technology library
Logic function
Technology mapping
Gate-level
netlist
•••
•••
•••
Convert logic function into gate-level netlist
Comply with technological constraints
  Path balancing
  Limited fanout
  Timing constraints
Optimize target metrics
  Area
  Delay

## Slide 38
Convert logic function into gate-level netlist
Comply with technological constraints
  Path balancing
  Limited fanout
  Timing constraints
Optimize target metrics
  Area
  Delay
()E
Technology Mapping 101
A
B
C
D
E
X

## Slide 39: Technology Mapping 101
Convert logic function into gate-level netlist
Comply with technological constraints
  Path balancing
  Limited fanout
  Timing constraints
Optimize target metrics
  Area
  Delay
()E
A
B
C
D
E
∧
∧
∧
∧
∧
∧
X
A
B
C
D
E
X

## Slide 40: Technology Mapping
A
B
C
D
E
∧
∧
∧
∧
∧
∧
X
A
B
C
D
E
X
Using technology library
  Area and delay information
Convert technology-independent logic function,
Into technology-dependent network
Comply with technological constraints
  Path balancing
  Limited fanout
  Timing constraints
Optimize target metrics
  Area
  Delay
Area=23 |  |  |  | 
1 cycle |  |  |  | 
x | 1 | 0 | 1 | 0
y | 1 | 1 | 0 | 0
f | 1 | 0 | 0 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A
B
C
D
E
X
Area=11 |  |  |  | 
1 cycle |  |  |  | 
x | 1 | 0 | 1 | 0
y | 1 | 1 | 0 | 0
f | 0 | 1 | 1 | 0
Area=14 |  |  |  |  |  |  |  | 
0 cycles |  |  |  |  |  |  |  | 
x | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
y | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
z | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
f | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
Notes: Remove 37-38
Explain

## Slide 41: Technology Mapping
A
B
C
D
E
∧
∧
∧
∧
∧
∧
X
A
B
C
D
E
X
Using technology library
  Area and delay information
Convert technology-independent logic function,
Into technology-dependent network
Comply with technological constraints
  Path balancing
  Limited fanout
  Timing constraints
Optimize target metrics
  Area
  Delay
Area=23 |  |  | 
1 cycle |  |  | 
1 | 0 | 0 | 0
x | y | f
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
x | y | z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A
B
C
D
E
X
Area=11 |  |  | 
1 cycle |  |  | 
0 | 1 | 1 | 0
Area=14 |  |  |  |  |  |  | 
0 cycles |  |  |  |  |  |  | 
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 42: Precompute Technology Library
a [0]
b [0]
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
+ |  | 
+ |  | 
+ |  | 
+ |  | 
+ |  | 
Function | Area | Delay
Notes: Explain truth tables to represent functions
Don't use TT, use DNF sum of products

## Slide 43: Precompute Technology Library: AA
M
a+b [7]
Area=7
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
+ | 7 | 0
+ |  | 
+ |  | 
+ |  | 
+ |  | 
Function | Area | Delay
 | 7 | 0
a [0]
b [0]

## Slide 44: Precompute Technology Library: AS
a [0]
a+b [7]
Area=9
b [0]
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
+ | 7 | 0
+ |  | 
+ |  | 
+ |  | 
+ |  | 
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 7 | 0

## Slide 45: Precompute Technology Library: AS
a [0]
b [0]
Area=10
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
+ | 7 | 0
+ |  | 
+ |  | 
+ |  | 
+ | 10 | 1
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 7 | 0
 | 10 | 1
a [0]
a+b [7]
Area=9
b [0]

## Slide 46: Precompute Technology Library: SA
0010[17]
0100[17]
Area=7
a [0]
b [0]
Area=6
Area=7
ab [19]
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 22 | 1
 | 22 | 1
 | 19 | 1
+ | 7 | 0
+ | 22 | 1
+ | 22 | 1
 | 25 | 1
+ |  | 
+ | 10 | 1
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 22 | 1
 | 22 | 1
 | 19 | 1
 | 7 | 0
 | 22 | 1
 | 22 | 1
 | 25 | 1
 | 10 | 1

## Slide 47: Precompute Technology Library: AA
0010[17]
0100[17]
CB
s
CB
s
AA
AS
SA
AA
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 22 | 1
 | 22 | 1
 | 19 | 1
+ | 7 | 0
+ | 22 | 1
+ | 22 | 1
 | 25 | 1
+ | 42 | 1
+ | 10 | 1
Function | Area | Delay
 | 9 | 1
 | 9 | 1
 | 16 | 1
 | 22 | 1
 | 22 | 1
 | 19 | 1
 | 7 | 0
 | 22 | 1
 | 22 | 1
 | 25 | 1
 | 42 | 1
 | 10 | 1
M
Area=7

## Slide 48: Technology Mapping
A
B
C
D
E
∧
∧
∧
∧
∧
∧
X
Precompute library of optimal structures
  Only done once
  Can be reused
Apply library to create gate-level netlist
Area=23 |  |  | 
1 cycle |  |  | 
1 | 0 | 0 | 0
A
B
C
D
E
X
Area=11 |  |  | 
1 cycle |  |  | 
0 | 1 | 1 | 0
Area=14 |  |  |  |  |  |  | 
0 cycles |  |  |  |  |  |  | 
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
A
B
CB
CB
C
D
E
X
Notes: We perform tech mapping
Boolean network with simple operations -> LUT mapping
(Simplify)
Apply enumeration to create library of optimal compound gates
Only once for
Apply library to create a gate netlist
(say)
Satisfy all sync requirements
Example on the right
Do not mention LUTs

## Slide 49: Depth Reduction
A
B
C
D
E
A
B
CB
CB
C
D
E
Conventional RSFQ
10 elements
4 cycles
Gate compounding RSFQ
6 elements
1 cycle

## Slide 50: Results
Enumerated all 65,536 4-input functions
48x 2.5GHz Intel Xeon E5-2680 CPU
256GB of RAM
52 hour runtime
[5] https://github.com/lsils/mockturtle
[6] G. Pasandi and M. Pedram, "PBMap: A Path Balancing Technology Mapping Algorithm for Single Flux Quantum Logic Circuits," in IEEE TASC 2019
Mapped with mockturtle library [6]
EPFL and ISCAS benchmarks
On average vs state of the art [7]
  24% smaller area
  33% smaller depth
Notes: Spend more time on AA AS SA
One slide for enumeration
show a compound gate
Remove #DFF section
Highlight reduction in table
Mention that we count all of the DFFs
Emphasize #JJs and delay

## Slide 51: Summary
RSFQ can bring enormous improvements in power and speed
Gate compounding simplifies path balancing of RSFQ circuits
  Smaller logic depth
  More functionality in fewer clock cycles
Enumerate database of optimal small-scale structures up to 4 inputs
  Apply to construct large scale networks
Smaller area and depth w.r.t. state-of-the-art
Notes: Remove path balancing
Gate compounding - simplifying the balancing of circuits

## Slide 52: Thank you!